  System A

- Extruded aluminium support structure: Surface treatment

  - Polyester powder coating RAL______

  - Natural anodised

- U-shaped rollformed aluminium carriers

  - Panelcarrier SL-2, module 74 mm, shadow angle 66°

  - Panelcarrier SL-4, module 86 mm, shadow angle 69°

  System B

- Modilar panel brackets of extruded aluminium

  - Spacer 48 mm, module 74 mm, shadow angle 67°

  - Spacer 63 mm, module 89 mm, shadow angle 57°

  - Spacer 88 mm, module 114 mm, shadow angle 45°

  System C

- Extruded aluminium support structure: Surface treatment

  - Polyester powder coating RAL______

  - Natural anodised

- U-shaped rollformed aluminium carriers

  - Panelcarrier SL-4, module 86 mm, shadow angle 69°

  - Panelcarrier SL-5, module 74 mm, shadow angle 67°

  - Panelcarrier H-3, module 69 mm, shadow angle 90°

  System D

- Extruded aluminium support structure: Surface treatment

  - Polyester powder coating RAL______

  - Natural anodised

- Modular panel brackets of extruded aluminium

  - Spacer 48 mm, module 71 mm, shadow angle 83°

  - Spacer 63 mm, module 86 mm, shadow angle 68°

  - Spacer 88 mm, module 111 mm, shadow angle 50°

| Panels: |
| --- |
| Shape: | C-shaped, 84 mm wide panels with half round edges |
| Panel section: | 84 x 16 mm, thickness 0.6 mm |
| Panel length: | max. 6000 mm |
| Alloy: | EN-AW 3005 |
| Surface treatment: | Frontside: Luxacote® finish, 3 layer, 40 mµ, colours; see colour chart Backside: polyester coating, standard white |
| Installation: | Panels are clipped on the carriers or panel brackets |