| Product : | HunterDouglas® Sun Louvre System 100R |
| --- | --- |
| System: | Fixed canopy or façade louvre system |
| Shape: | Aluminium extruded C-shaped panel |
| Panel section: | 101 x 26 mm, thickness 1.8 mm |
| Panel length: | max. 6000 mm |
| Support: | Aluminium extruded HunterDouglas® SLR carrier profile |
| Alloy extrusions: | Al-Mg-Si 0.5 F22 (EN-AW 6060 T6/T66) |
| Horizontal application: | Spacer 0 mm, module 90 mm, shadow angle 69° Spacer 30 mm, module 120 mm, shadow angle 53° |
| Vertical application: | Spacer 0 mm, module 90 mm, shadow angle 11° Spacer 30 mm, module 120 mm, shadow angle 34° |
| Angle of panels: | 60° (canopy configuration) 45° (façade louvre configuration) |
| Panel fixing: | Polycarbonate brackets, 60° or 45° angle in combination with spacers to increase module |
| Fascia (option): | Matching aluminium extruded fascia profile 25 x 240 x 25 mm, fixing concealed |
| Finish: | Natural anodised 20 microns (VOM1/A20/VB6) Custom colour anodised (limited range) 20 microns Polyester powder coated to RAL or other industry standard colour, thickness 60 or 90 microns, gloss 70% |
| Support fixation: | Support fixed to façade by means of hot dip galvanised steel console, with extra aluminium top brace as an option. |