## PART 1: GENERAL

  - INTRODUCTION

Supply and fix Luxalon® Exterior Closed Ceiling system as manufactured by Hunter Douglas Architectural Products.

2.2 DESCRIPTION OF THE SYSTEM

The system will consist of linear panels fixed to an adjustable suspension system, in combination with locking clips, which allows for individual panels to be removed by using a dismounting tool. Panels of different widths can be combined in the ceiling, if desired. To prevent contact corrosion by applying dissimilar metals, each fixing of the carriers to the sub construction must be made through the Luxalon® washer set.

## PART 2: PRODUCT

_________ m² Luxalon® Exterior Closed Ceiling, consisting of:

2.1 PANELS

- 75C, size 75 x 15,5 mm, to be manufactured from 0.6 mm thick Aluminium

- 150C, size 150 x 15,5 mm, to be manufactured from 0.6 mm thick Aluminium

- 225C, size 225 x 15,5 mm, to be manufactured from 0.6 mm thick Aluminium

Panels to be manufactured from pre-painted, stove enamelled aluminium, corrosion resistant alloy EN-AW 3005 or equivalent (according to EN 1396 and ECCA). Panels have a length of _________ mm (manufactured availability 1000-6000 mm). Panels to be coupled in longitudinal direction by means of panel splices.

2.2 SUSPENSION

Rows of 0.95 Alu roll formed carriers shall be installed at _________ centre on centre by means of a levelled suspension of sufficient strength and rigidity to provide resistance to wind pressure/wind suction, at a distance of _________, centre on centre. Carriers will be joined by means of carrier splices. Carriers provided with prongs to hold panels in a module which is a multiple of 75 mm. Panels are locked to the carrier by crosswise installed separate locking clips.

## PART 3: ADDITIONAL SPECIFICATIONS

### PERIMETER PROFILES

- Wall L-profile 29.2 x 19.4 mm made of 0.5 mm thick aluminium

- Wall L-profile 45 x 18.5 mm made of 0.8 mm thick aluminium

- Wall W-profile 45 x 21 x 21 x 18.5 mm made of 0.8 mm thick aluminium

3.2 COATING

Architect will make a colour selection from the standard Hunter Douglas colour range for Luxalon® Exterior 75/150/225C panels code no._________ or a special colour will be made to match.

The coating will consist of the tough and durable Luxacote® finish in nominal thickness of approximately 20 microns, applied in a continuous coil coating process ensuring uniform coating thickness. The Luxacote® finish guarantees optimum adhesion and excellent resistance to weathering.

3.3 INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications or shown on the drawings.