## PART 1. GENERAL

  - INTRODUCTION

Supply and fix type “TREND” or “STANDARD”, concealed or exposed, Veneered Wood Wall Panel System as manufactured by Hunter Douglas Architectural.

  - DESCRIPTION OF THE SYSTEM

The system will consist of wood veneer panels, mounted onto an Omega profile or wooden batten substructure, with the use of metal clips.

## PART 2. PRODUCT

  - VENEERED WOOD PANELS

________m2 type “TREND” or “STANDARD” concealed or exposed Veneered Wood Wall Panels, consisting of:

Bevelled edged (TREND) or square edged (STANDARD) panels which are 600x600mm or 1200x600mm. The panels have a 16mm thick FR treated MDF (B,S1-d0) core veneered with 0.6mm thick slip/book matched veneer on the visible side. A 0.6mm compensating veneer is adhered to the reverse of the tile. The bevelled edged panels (TREND) have a 0mm joint, whereas the square edges panels (STANDARD) have a 5/10/15/20/30mm joint, which will be closed with a melamine strip.

  - FIXATION

The panels are fixed with the use of screw clips, creating a 0/5/15/20/30mm joint. For fixation on an Omega profile, special turn clips can be used, creating a 0/5/10mm joint.

## PART 3: ADDITIONAL SPECIFICATIONS

  - PERFORATIONS

Manufacturer shall supply panels with perforation pattern type_______ with a nominal  plain border on all sides.

Perforations will have a ____ diameter hole in a regular/irregular pattern or ____ diameter slot with a ____mm length in a regular/irregular pattern resulting in a ____% open area.

  - ACOUSTICS

Manufacturer shall/shall not supply acoustic non woven textile, thickness 0.2mm  glued on reverse tile side.

  - VENEER TYPES

Panels shall be supplied with crown/quarter cut veneer ___________ slip/book matched selected from the Hunter Douglas veneer selector or a special veneer.

Samples shall be supplied for approval prior to order.

The veneer is lacquered with a UV-polyacrylate varnish.

  - INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications or shown on the drawings.

  - SUBSTITUTIONS

Ceiling installers wishing to submit proposals on systems other than the Hunter Douglas Veneered Wood Wall Panel shall, at least 10 days in advance of the bid date, submit to the architect complete descriptive information of the total system and performance data of tests made as a system. In addition include a list of similar installations of the proposed substitution. If approval is made an addendum will be issued enumerating such approved system as herein set forth.